## Slide 1: SystemLink Cloud: an Introduction
www.originalcode.com
Presented by David Thomson, PhD
Original Code Consulting LLC
dthomson@originalcode.com
www.originalcode.com

## Slide 2: WebVI – Why?
CU Atmospheric Test Chamber – status webpage
Replacement for Data Dashboard running on an Android tablet
Web page accessible from any device with a web browser
Now (finally!) able to create a full web page from within LabVIEW
www.originalcode.com

## Slide 3: What is SystemLink Cloud?
Helium
Web Browser
LabVIEW 2015
www.originalcode.com
SystemLink
SystemLink Cloud
NI Web Server
NI Package Manager
SystemLink Server
SystemLink Client
WebVIs
LabVIEW NXG
Tags
Messages
Skyline
API Key
NXG Web Module

## Slide 4: New NI Technologies
SystemLink – new software tool for managing distributed systems of hardware, software, and data
  http://www.ni.com/en-us/shop/select/application-software-for-data-acquisition-and-control-category
NI Package Manager – new tool for deploying NI (and other) software
  (Eventually replacing VIPM?)
  Need this for almost all software technologies described in this presentation
SystemLink Server – server software for running SystemLink and a whole lot of other stuff…uh…
SystemLink Client – a smaller package of software for using SystemLink stuff from the client perspective…uh…uh…
www.originalcode.com

## Slide 5: New NI Technologies, cont…
SystemLink Cloud – a new tool for hosting SystemLink stuff on NI’s servers and for…uh…uh…stuff with API Keys, and uh…
  NOTE: This is a Tech Preview program. It has not been officially released yet.
Skyline Data Services – a new set of APIs for sharing data across applications and devices (e.g. networked)
  Tags (most recent value, DBL, INT, STR)
  Messages – strings - ???
  Maybe also includes Files???
www.originalcode.com

## Slide 6: WebVIs
Finally! We can build web pages in LabVIEW!
WebVI is a special entity in NXG, not the same as a GVI
A WebVI is built into a web page using a special distribution
Can add CSS, HTML, Javascript etc. to a WebVI
WebVIs can be built in LV NXG 2.x
  (SystemLink Cloud requires LV NXG 2.1)
Must have a license for the NXG Web Module
www.originalcode.com

## Slide 7: WebVIs
Can host a WebVI on ANY webserver...
…unless you want to use Skyline Data Services!
In which case you must host it on NI Web Server with SystemLink Server or on SystemLink Cloud
  (Currently, there is no tool to install the Skyline Data Services Server other than the NI Web Server Installer)
SystemLink has many other features, and is not really intended for just casual web page hosting
  10 seat access license is $2000/yr – 25 set is $5000/yr, perpetual licenses are 2 or 2.5 times that
www.originalcode.com

## Slide 8: SystemLink Cloud
Currently a Tech Preview program
WebVI hosting in the cloud
Included with Web Module
Can host 20 WebVIs, 10,000 Tags, and unlimited Messages
Your SystemLink Cloud account (in the system referred to as Helium) is linked to your NI.com credentials
www.originalcode.com

## Slide 9: Security
Can limit access to a WebVI by requiring the account’s NI.com credentials
Or can make a WebVI public and open to anyone with the URL
Can limit access to various Tags and Messages by linking them to an API Key which has policies defined for it
www.originalcode.com

## Slide 10: How to Create a Working WebVI
Join the Tech Preview: http://www.ni.com/en-us/support/software-technology-preview.html (tell them ALARM sent you)
Get an account on Helium: https://www.systemlinkcloud.com/
Download and install NXG 2.1 and the NXG API using NI Package Manager: https://www.systemlinkcloud.com/api-download
Get an API Key: https://www.systemlinkcloud.com/security
Store your API Key someplace safe, you are only shown it once!
www.originalcode.com

## Slide 11: How to Create a Working WebVI
Use NXG to create a WebVI
  I use Tags to transfer data from LabVIEW to the WebVI
Build the WebVI into a Package
Upload the Package to the SystemLink Cloud: https://www.systemlinkcloud.com/webapphosting
Run the link for the WebVI in a web browser
www.originalcode.com

## Slide 12: How to Send Data Between your WebVI & LV
I wanted to send data to a web page from LV 2015
Luckily, LV 2015 IS supported by Skyline Data Services. (It is the oldest supported version of LV)
Install the Skyline API by (I think…) installing the SystemLink Client using NI Package Manager (this was an extra step for me, since my LV 2015 is not on the same machine as NXG)
Inside LV 2015, you need an off-palette Open VI to use SystemLink Cloud instead of SystemLink:
  C:\Program Files (x86)\National Instruments\LabVIEW [Version]\vi.lib\Skyline\Configuration\Configuration HTTP_class\Open Configuration API Key.vi
  https://github.com/ni/webvi-examples/tree/master/UtilizeSkylineDataServices
www.originalcode.com

## Slide 13: How to Build the Web App
File/New/Distribution
On the Document tab of the Distribution, select Web Server as Target
Select Package for Output Type
On the Distribution tab, press the Add button for Applications/Libraries
Add Company and Product info, etc.
Save all
Build
www.originalcode.com

## Slide 14: Example Time…
www.originalcode.com

## Slide 15: DataDashboard
www.originalcode.com

## Slide 16: Caveats and Issues
There are Multi-Read and Multi-Write VIs to allow a single html POST to handle multiple tags
  This is supposed to improve performance
  In NXG, you can define the “group” and then add values to it later
  I haven’t tested the performance there yet…
  In LV 2015, you create the “group” with their values, e.g. every time you do the Multi-Write
  This is slow!
  This may get better. Skyline is young. But how much support they’ll put into LV 2015????
www.originalcode.com

## Slide 17: Caveats and Issues
Limited functionality in NXG/WebVIs
  No event structure
  No property nodes
  Limited graphing functionality
www.originalcode.com

## Slide 18: Advantages
Should continue to improve and be supported
DataDashboard was limited in range by network access to the Shared Variables (there are ways to fix this…) whereas the Cloud is accessible across the Internet
Can program logic behind the front panel
It’s LabVIEW!!!!
www.originalcode.com